Laboratory work #3

Researching diode limiters and diode clipping circuits (Workbench computer modulation)

Task 1

Measuring the voltage limiting level of a series diode limiter

Fig.3.1 Series diode limiter

Construct the circuit according to Fig.3.1 and switch it on.

Your task is to write the readings of the following values:

- input and output voltage oscillograms

- max value of the input voltage amplitude

- max value of the output voltage amplitude

- the voltage limiting level.

Task 2

Measuring the voltage limiting level of a series biased diode limiter

Fig.2 Series biased diode limiter

a) Measuring the voltage level at positive bias.

Construct the circuit according to Fig.3.2 and switch it on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

b) Measuring the voltage level at negative bias.

Change the polarity of the power source (5V) and switch the circuit on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

Task 3

Measuring the voltage limiting level of a shunt diode limiter

Fig.3.3 The shunt diode limiter.

Construct the circuit according to Fig.3.3 and switch it on.

Your task is to write the readings of the following values:

- input and output voltage oscillograms

- max value of the input voltage amplitude

- max value of the output voltage amplitude

- the voltage limiting level.

Task 4

Measuring the voltage limiting level of a shunt biased diode limiter

Fig.3.4 The shunt biased diode limiter.

a) Measuring the voltage level at positive bias.

Construct the circuit according to Fig.3.4 and switch it on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

b) Measuring the voltage level at negative bias.

Change the polarity of the power source (5V) and switch the circuit on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

Task 5

Measuring the voltage limiting level of a shunt biased zener diode limiter

Fig.3.5 The shunt biased zener diode limiter

Construct the circuit according to Fig.3.5 and switch it on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

Task 6

Measuring the voltage limiting level of a symmetric shunt biased zener diode limiter

Fig.3.6 The symmetric shunt biased zener diode limiter

Construct the circuit according to Fig.3.6 and switch it on.

Write the following readings:

- max value of  the input voltage

- max value of  the output voltage

- the limited voltage level.

Task 7

Measuring the value of the output voltage constant component of a positive diode forming circuit

Fig.3.7 The positive diode forming circuit

During the 1st half-wave of the input voltage a current is passing through the diode.

The capacitor will charge up to the level of - 0.7V (this voltage level is less than the input voltage by the value of the direct voltage drop across the diode).

Thus, during the positive half-wave the diode is closed.

Within the period of oscillation the capacitor will discharge slightly and charge again within the negative half-wave.

We obtain the constant voltage component as a result of the mentioned process.

It’s necessary to have the value of RC-circuit time constant to exceed substantially the input signal period.

Construct the circuit according to Fig.3.7 and switch it on.

Write the following readings:

- input and output voltage oscillograms

- max and min values of the input voltage amplitude

- max and min values of the output voltage amplitude

- the constant component of the output voltage amplitude.

Task 8

Measuring the constant component of the output voltage of a positive diode forming circuit at the increase in the input voltage amplitude.

Construct the circuit according to Fig.3.7, set the value of the generator equal to 8V and switch it on.

Write the following readings:

- input and output voltage oscillograms

- max and min values of the input voltage amplitude

- max and min values of the output voltage amplitude

- the constant component of the output voltage amplitude.

Task 9

Measuring the constant component of the output voltage of a positive diode forming circuit at the reduction in the input voltage amplitude.

Construct the circuit according to Fig.3.7, set the value of the generator equal to 2V and switch it on.

Write the following readings:

- input and output voltage oscillograms

- max and min values of the input voltage amplitude

- max and min values of the output voltage amplitude

- the constant component of the output voltage amplitude.

### Your report must contain the characteristics of the diodes in question, their circuits and the obtained results.

### Question list.

## The properties of p-n junction

### Shockley diode equation

The characteristics of diodes

### Rectifying Diodes

### Half-wave rectifiers

### Full-wave rectifiers

Bridge rectifiers

### Voltage Regulating Diodes

### Diodes as frequency multipliers

### Diodes as mixers

### Applications of switching Diodes

### Light-Emitting-Diodes or LED's

Laser diodes

## Zener diodes

## Application of zener diodes