Laboratory work #10

## RESEARCHING OPERATIONAL AMPLIFIERS

Task 1

Measuring the input currents

Fig.10.1

Construct the circuit according to Fig.10.1.

The current of the non-inverting input =________________

The current of the inverting input =________________

The mean input value =________________

The difference of input currents ___________

Task 2

Measuring the bias voltage

Fig.10.2

Construct the circuit according to Fig.10.2.

Define the bias voltage  taking into account the amplification coefficient.

The amplifier’s output voltage  _______________

The amplification coefficient (calculation)  _________________

The bias voltage  (calculation) _________

Task 3

Measuring the input and output resistances

- Construct the circuit according to Fig.10.3.

Measure the input current and output voltage.

The input current before switching the key()____________

The input current after switching the key()____________

The change in the output voltage, mV (calculation) ______________

The change in the input current, (calculation) ______________

The input differential resistance (incremental resistance) (calculation)

______________

Fig.10.3

b) Decrease R2 until(about half of the output voltage at a point).

The output voltage  =  __________V

The output resistance  __________

Task 4

Construct the circuit according to Fig.10.4.

Fig.10.4

Draw the out voltage oscillograms.

Using these oscillograms define the output voltage, the settling time of the output voltage and the rate of the rise in the output voltage V/microsec.

The output voltage  _______________

The settling time of the output voltage  _______________

The rate of the rise in the output voltage __________

The oscillograms of the input and output voltages

Your report must contain the circuits and characteristics of BJT.

Question list

Differential amplifiers

Building a differential amplifier

The instrumentation amplifier

# The "operational" amplifier

Negative feedback of operational amplifiers

# Divided feedback

# An analogy for divided feedback