Laboratory work #7

## Researching the BJT operating point FOR the common-emitter circuit

Task 1.

Repeat CUT-OFF, SATURATION and LINEAR modes of BJT (Practice work #2).

Task 2

## Researching the BJT operating point for the common-emitter circuit using a base resistor feedback circuit

Fig.7.1

Repeat the linear mode of BJT (Construct the circuit according to Fig.7.1 and switch it on.

- Write the readings of, , , .

b) Define the following values (the value of may be taken from the previous laboratory work):

Base current _____

Collector current ______

Base-emitter voltage _____

Collector-emitter voltage _____

c) Construct the load line regarding the constant current for the output characteristic (BJT 2N3904, the value ofand other data may be taken from the previous laboratory work). Define the location of (Q) point on the load line.

Base current _____

Collector current ______

Collector-emitter voltage _____

d) Mark on the curve the operating point location before and after the change in the BJT current gain.

Base current _____

Collector current ______

Collector-emitter voltage _____

e) Defining the base-collector resistance.

Base current _____

Collector current ______

Collector-emitter voltage _____

Task 3

Researching the parameters of the operating point by setting the base current using a voltage divider

Construct the circuit according to Fig.7.2 and switch it on.

Fig.7.2

a) Write the readings of, , ,, , define the value of.

Base current _____

Collector current ______

Emitter current ______

Collector-emitter voltage _____

_____

b) For the operating point

________

Collector current ______

Emitter current ______

Collector-emitter voltage _____

c) Construct the load line for constant current and define the location of Q point (before and after changing the value of.

Base current _____

Collector current ______

Collector-emitter voltage _____

d)  relation

________

Base current _____

Collector current ______

Collector-emitter voltage _____

Task 4

Researching the parameters of the operating point by setting the base current using a resistor in the base-collector circuit

Construct the circuit according to Fig.7.3 and switch it on.

a) Write the readings of, , ,, , define the value of.

Base current _____

Collector current ______

Emitter current ______

Collector-emitter voltage _____

_____

Fig.7.3

b) Define the collector current.

c) Construct the load line for the output characteristics (2N3904 BJT). Define the operating point (Q) and mark its location on the curve.

Your report must contain the circuits and characteristics of BJT.

# Question list

CUT-OFF, SATURATION and LINEAR modes

Common emitter amplifiers

Common collector (emitter follower) amplifier

### Biasing technique

### Base Bias

### Collector-feedback bias

### Emitter-bias

### Voltage divider bias

Bias for a cascode amplifier.

Common emitter amplifiers with feedback