# Laboratory work #8

Researching BJT amplifiers

Task 1.

Researching Common Emitter Amplifier

Construct the circuit according to Fig.7.1 and switch it on.

Apply sine-wave voltage to 1st node (=1000 Hz and V=10 mV).

Fig.8.1 BJT Common Emitter Amplifier circuit

а) Plug the oscillograph between 1 and 6 nodes.

b) Switch on the simulation mode.

c) Control the correspondence between the input and output voltages (in the case of the output signal distortion it’s reasonable to diminish the input signal amplification).

d) Measure the voltages at following nodes:

– - the input voltage;

-  – the voltage at node 2;

-  – the voltage at node 6.

Define:; ( = 100 Ohms),

.

Table 8.1

| mV | mV | mV | Ohm |  | dB | mV | mА | Ohm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |  |  |  |

- the idle mode;

- the short circuit.

Table 8.1 contains the obtained results.

e) Define using the obtained values.

f)  Draw the oscillograms at 1-6 nodes.

g) Obtain necessary results and plot the amplifier’s amplitude characteristic at the input frequency =1000 Hz and =10, 20, 50…2000 mV. Set data into Table 8.2.

Table 8.2

| , mV | , mV | , mV | , mV | , Ohm |  |
| --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |
| 20 |  |  |  |  |  |
| 50 |  |  |  |  |  |
| 200 |  |  |  |  |  |
| 500 |  |  |  |  |  |
| 1000 |  |  |  |  |  |
| 2000 |  |  |  |  |  |

h) Set the value of =500 mV and changing the input frequency (=1,10,50,102,103,104,105 Hz) measure the voltage at 6 node and complete Table 7.3.

Gain frequency characteristic .

Table 8.3

| , Hz | , mV | , mV |  |  |
| --- | --- | --- | --- | --- |
| 1 | 500 |  |  |  |
| 10 | 500 |  |  |  |
| 102 | 500 |  |  |  |
| 103 | 500 |  |  |  |
| 104 | 500 |  |  |  |
| 105 | 500 |  |  |  |

Task 2.

Researching common-collector amplifier.

Fig.8.2

Construct the circuit according to Fig.8.2.

Set the value of the input frequency = 1000 Hz and input voltage = 10 mV.

Carry out the items a)…h) and complete the Tables 8.4, 8.5, 8.6.

Calculate , , .

Table 8.4

| , mV | , mV | , mV | , Ohm |  | , dB | , mV | , mA | , Ohm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |  |  |  |

Table 8.5

| , mV | , mV | , mV | , mV | , Ohm |  |
| --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |
| 100 |  |  |  |  |  |
| 1000 |  |  |  |  |  |
| 5000 |  |  |  |  |  |
| 8000 |  |  |  |  |  |
| 10000 |  |  |  |  |  |

Table 8.6

| , Hz | , mV | , mV |  |  |
| --- | --- | --- | --- | --- |
| 1 | 500 |  |  |  |
| 10 | 500 |  |  |  |
| 102 | 500 |  |  |  |
| 103 | 500 |  |  |  |
| 104 | 500 |  |  |  |
| 105 | 500 |  |  |  |

Task 3.

Researching common-base amplifier.

Fig.8.3

Construct the circuit according to Fig.8.3.

Set the value of the input frequency = 1000 Hz and input voltage = 10 mV.

Carry out the items a)…h) and complete the Tables 8.7, 8.8, 8.9.

Calculate , , .

Table 8.7

| , mV | , mV | , mV | , Ohm |  | , dB | , mV | , mA | , Ohm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |  |  |  |

Table 8.8

| , mV | , mV | , mV | , mV | , Ohm |  |
| --- | --- | --- | --- | --- | --- |
| 10 |  |  |  |  |  |
| 100 |  |  |  |  |  |
| 1000 |  |  |  |  |  |
| 5000 |  |  |  |  |  |
| 8000 |  |  |  |  |  |
| 10000 |  |  |  |  |  |

Table 8.9

| , Hz | , mV | , mV |  |  |
| --- | --- | --- | --- | --- |
| 1 | 500 |  |  |  |
| 10 | 500 |  |  |  |
| 102 | 500 |  |  |  |
| 103 | 500 |  |  |  |
| 104 | 500 |  |  |  |
| 105 | 500 |  |  |  |

Task 4.

Calculate the comparative characteristics of BJT amplifiers

Table 8.10

| Parameter | Units | Reference designation | BJT amplification stages |
| --- | --- | --- | --- |
|  |  |  | CE | CC | CB |
| Input resistance | Ohm |  |  |  |  |
| Output resistance | Ohm |  |  |  |  |
| Voltage amplification coefficient | - |  |  |  |  |

Your report must contain the circuits and characteristics of BJT.

# Question list

## Introduction to Amplifiers

### Amplifier Gain of the Input Signal

## Power Amplifiers

## Amplifier Classes

## Class A Operation

## Class B Operation

## Class C Operation

### Darlington Transistor Configurations

### Transformer-coupled Amplifier Circuit

### Class B Push-pull Transformer Amplifier Circuit

Sziklai pair transistor configuration