Laboratory work #6

# Researching the properties of bipolar junction transistors

Task 1.

Researching the ratio of collector current to base current.

Construct the circuit according to Fig.6.1 and switch it on.

Fig.6.1

а)  Write the values of  , , and calculate the value of .

b) Set the value of = 2.68V. Write the values of, , and calculate the value of .

c) Set the value of  = 5V. Write the values of, , and calculate the value of .

Table 6.1

| # | voltage | voltage | voltage | Base current | Collector current |  |
| --- | --- | --- | --- | --- | --- | --- |
| а) | 10V | 5.7V |  |  |  |  |
| б) | 10V | 2.68V |  |  |  |  |
| в) | 5V | 2.68V |  |  |  |  |

Task 2.

Researching the collector reverse current.

Use the circuit Fig.6.1 and set the value of =0V.

Write the values of for the set values of and.

The reverse collector current

=_____

=______

=_____

Task 3.

Researching the BJT output characteristics for the common emitter circuit.

Construct the circuit according to Fig.6.2 and switch it on.

a) Measure for each value ofand.

Table 6.2

| , V | , А |
| --- | --- |
|  | 0 | 20 | 40 | 60 | 80 | 100 |
|  | , mА |
| 0 |  |  |  |  |  |  |
| 0.5 |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| 5.5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |

b) Using the obtained characteristics define the value of  at the change in  from 10А to 30А (=10V).

Fig.6.2

Task 4.

Obtaining BJT input characteristic for the common emitter circuit.

Construct the circuit according to Fig.6.3 and switch it on.

Fig.6.3

а) Set =10V. Measure ,,, for various values of  according to Table 6.3.

b) Using Table 6.3 construct the plot describing the dependence of on .

c) Using the input characteristic defineat the change in the from 10 to 30A.

Table 6.3

| , V | , V |
| --- | --- |
|  | 0 | 2 | 4 | 6 | 8 | 10 |
|  | , А |
| 0 |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |

The calculated value of  =____

Task 5.

Obtaining BJT input characteristic for the common base circuit.

Construct the circuit according to Fig.6.4 and switch it on.

а) Using Table 6.4 plot diagram.

b) Using the obtained characteristic define  at the change in from 5 to 10 mA.

c) Define using the formula (take the values of from Table 6.4 on condition that .

Fig.6.4

Table 6.4

| , V | , V |
| --- | --- |
|  | 0 | 2 | 4 | 6 | 8 | 10 |
|  | , mА |
| 0 |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| …… |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |

Your report must contain the circuits and characteristics of BJT.

# Question list

# Bipolar Junction Transistors

# Transistor as Current Amplifier

Common-Base (CB)

Common-Emitter (CE)

BJT quirks

### Temperature drift

### Thermal mismatch (problem with paralleling transistors)

### High frequency effects

### Miller’s theorem