### Laboratory work #13

RESEARCHING RECTANGULAR PULSE GENERATORS

Task 1

Researching BJT multi-vibrators

Fig.13.1

a) Construct the circuit according to Fig.13.1. Switch on the circuit.

Depict the oscillograms at 1, 2, 3, 4 points.

The oscillograms at 1, 2, 3, 4 points

b) Measure the amplitude, duty cycle and pulse period.

Calculate the duty cycle.

Pulse amplitude Um=_______V

Pulse period T= ______sec

Duty cycle Q= ______%

c) Link up С3 and С4 capacitors in parallel to С1 and С2 ones through SA2 and SA3 switches.

Depict the oscillograms at 1, 2, 3, 4 points.

The oscillograms at 1, 2, 3, 4 points

d) Measure the amplitude, duty cycle and pulse period.

Pulse amplitude Um=_______V

Pulse period T= ______sec

Duty cycle Q= ______%

e) Switch SA1.1 and SA1.2.

Depict the oscillograms at 2 and 3 points at various positions of SA2 and SA3 switchers.

The oscillograms at 2 and 3 points.

Task 2

Researching Operational Amplifiers multi-vibrators

a) Construct the circuit according to Fig.13.2. Switch on the circuit.

Set Е0=Е1=15V.

b) Depict the oscillograms at 1, 2, 3 points.

c) Measure the amplitude, duty cycle and pulse period.

Calculate the duty cycle.

Pulse amplitude Um=_______V

Pulse period T= ______sec

Duty cycle Q= ______%

d) Switch SA1 (Space) and depict the oscillograms at 1, 2, 3 points.

The oscillograms at 1, 2, 3 points

e) Measure the amplitude, duty cycle and pulse period.

Calculate the duty cycle.

Pulse amplitude Um=_______V

Pulse period T= ______sec

Duty cycle Q= ______%

f) Come to the conclusion regarding the effect of the values of feedback resistors on the pulse period and duty cycle of the Op.Ampl. multi-vibrator.

Fig.13.2

Your report must contain the circuits and characteristics of operational amplifiers.

Question list

## Astable multivibrator circuit

### Multivibrator frequency

### Protective components

## Bistable multivibrator circuit

Oscillators

Phase-Shift Oscillators

The Wien-Bridge Oscillator

The Colpitts Oscillator

Hartley oscillator

Clapp oscillator

Armstrong oscillator

Crystal-Controlled Oscillators

Oscillator Troubleshooting