### Laboratory work #14

RESEARCHING SINUSOIDAL GENERATORS

Task 1

Researching the Wien-bridge sinusoidal oscillators

Fig.14.1

a) Construct the circuit according to Fig.14.1. Switch on the circuit.

b) Measure the generator frequency (SA1 switcher is designed to start up the generation circuit).

The generation frequency

f = _______

c) Calculate the generation frequency.

The calculated frequency

fCALC =______

d) Obtain the generation frequency equal to 10 kHz (selecting the R and C values for the Wien-bridge).

Define the theoretical capacitor value for the Wien-bridge (f= 10kHz).

Compare the theoretical capacitor value and its value during the fitting procedure.

Define the errors in defining R and С values.

The fitted value R= ______   C= ________

The calculated values RCALC= ______  CCALC = _____

The error in calculating R and C ( %)

γR= _________ γC= __________

Task 2

Researching the sinusoidal oscillators using integrating circuits

Fig.14.2

а) Construct the circuit according to Fig.14.2. Switch on the circuit.

b) Obtain the voltage oscillograms at 1, 2, 3 points.

c) Measure the period of pulses.

Task 3

Researching the dropping saw-tooth voltage generator

Fig.14.3

а) Construct the circuit according to Fig.14.3. Switch on the circuit.

b) Obtain the voltage oscillograms at 1, 2, 3 points.

c) Define the period of pulses.

Task 4

Researching the growing saw-tooth voltage generator

Fig.14.4

а) Construct the circuit according to Fig.14.4. Switch on the circuit.

b) Obtain the voltage oscillograms at 1, 2, 3, 4 points.

c) Define the period of pulses.

Task 5

Researching the astable saw-tooth voltage generator

а) Construct the circuit according to Fig.14.5. Switch on the circuit.

Obtain the voltage oscillograms at 1, 2, 3, 4 points.

Define the period of pulses.

b) Set R2=90 к, R3=8 к.

Obtain the voltage oscillograms at 1, 2, 3, 4 points.

Define the period of pulses.

c) Come to the conclusion regarding the effect of the values of feedback resistors on the pulse form of generator.

Fig.14.5

Your report must contain the circuits and characteristics of operational amplifiers.

Question list

## Astable multivibrator circuit

### Multivibrator frequency

### Protective components

## Bistable multivibrator circuit

Oscillators

Phase-Shift Oscillators

The Wien-Bridge Oscillator

The Colpitts Oscillator

Hartley oscillator

Clapp oscillator

Armstrong oscillator

Crystal-Controlled Oscillators

Oscillator Troubleshooting