PRACTICAL CLASS 3.3

Theme: Rotary wing aerodynamics

3.3.1. Rotary wing aerofoils

Airfoils

A helicopter flies for the same basic reason that any conventional aircraft flies, because aerodynamic forces necessary to keep it aloft are produced when air passes about the rotor blades. The rotor blade, or airfoil, is the structure that makes flight possible. Its shape produces lift when it passes through the air. Helicopter blades have airfoil sections designed for a specific set of flight characteristics. Usually the designer must compromise to obtain an airfoil section that has the best flight characteristics for the mission the aircraft will perform.

Airfoil sections are of two basic types, symmetrical and nonsymmetrical. Symmetrical airfoils have identical upper and lower surfaces. They are suited to rotary-wing applications because they have almost no centre of pressure travel. Travel remains relatively constant under varying angles of attack, affording the best lift-drag ratios for the full range of velocities from rotor blade root to tip. However, the symmetrical airfoil produces less lift than a nonsymmetrical airfoil and also has relatively undesirable stall characteristics. The helicopter blade must adapt to a wide range of airspeeds and angles of attack during each revolution of the rotor. The symmetrical airfoil delivers acceptable performance under those alternating conditions. Other benefits are lower cost and ease of construction as compared to the nonsymmetrical airfoil.

Nonsymmetrical (cambered) airfoils may have a wide variety of upper and lower surface designs. Advantages of the nonsymmetrical airfoil are increased lift-drag ratios and more desirable stall characteristics. Nonsymmetrical airfoils were not used in earlier helicopters because the centre of pressure location moved too much when angle of attack was changed. When centre of pressure moves, a twisting force is exerted on the rotor blades. Rotor system components had to be designed that would withstand the twisting force. Recent design processes and new materials used to manufacture rotor systems have partially overcome the problems associated with use of nonsymmetrical airfoils.

Airfoil Sections

Rotary-wing airfoils operate under diverse conditions, because their speeds are a combination of blade rotation and forward movement of the helicopter. An intelligent discussion of the factors affecting the magnitude of rotor blade lift and drag requires a knowledge of blade section geometry. Blades are designed with specific geometry that adapts them to the varying conditions of flight. Cross-section shapes of most rotor blades are not the same throughout the span. Shapes are varied along the blade radius to take advantage of the particular airspeed range experienced at each point on the blade, and to help balance the load between the root and tip. The blade may be built with a twist, so an airfoil section near the root has a larger pitch angle than a section near the tip.

The chord line is a straight line connecting the leading and trailing edges of the airfoil.

The chord is the length of the chord line from leading edge to trailing edge and is the characteristic longitudinal dimension of the airfoil.

The mean camber line is a line drawn halfway between the upper and lower surfaces. The chord line connects the ends of the mean camber line.

The shape of the mean camber is important in determining the aerodynamic characteristics of an airfoil section. Maximum camber (displacement of the mean camber line from the chord line) and the location of maximum camber help to define the shape of the mean camber line. These quantities are expressed as fractions or percentages of the basic chord dimension.

Thickness and thickness distribution of the profile are important properties of an airfoil section. The maximum thickness and its location help define the airfoil shape and are expressed as a percentage of the chord.

The leading edge radius of the airfoil is the radius of curvature given the leading edge shape.

3.3.2. Rotary wing planforms

Common terms used to describe the helicopter rotor system are shown here. Although there is some variation in systems between different aircraft, the terms shown are generally accepted by most manufacturers. The system shown here is fully articulated:

Semi rigid types do not have a vertical or horizontal hinge pin. Instead, the rotor is allowed to teeter or flap by a trunnion bearing that connects the yoke to the mast:

The chord is the longitudinal dimension of an airfoil section, measured from the leading edge to the trailing edge.

The span is the length of the rotor blade from the point of rotation to the tip of the blade.

The vertical hinge pin (drag hinge) is the axis which permits fore and aft blade movement independent of the other blades in the system.

The horizontal hinge pin is the axis which permits up and down movement of the blade independent of the other blades in the system.

The trunnion is splined to the mast and has two bearings through which it is secured to the yoke. The blades are mounted to the yoke and are free to teeter (flap) around the trunnion bearings.

The yoke is the structural member to which the blades are attached and which fastens the rotor blades to the mast through the trunnion and trunnion bearings.

The blade grip retainer bearing is the bearing which permits rotation of the blade about its spanwise axis so blade pitch can be changed (blade feathering)

Blade Twist is a characteristic built into the rotor blade so angle of incidence is less near the tip than at the root. Blade twist helps distribute the lift evenly along the blade by an increased angle of incidence near the root where blade speed is slower. Outboard portions of the blade that travel faster normally have lower angles of incidence, so less lift is concentrated near the blade tip.

3.3.3. Angle of attack

Angle of attack is an aerodynamic angle and is illustrated here:

It is defined as the angle between the airfoil chord and its direction of motion relative to the air (resultant relative wind). Several factors may cause rotor blade angle of attack to change. Some are controlled by the pilot and some occur automatically due to the rotor system design. Pilots are able to adjust angle of attack by moving the cyclic and collective pitch controls. However, even when these controls are held stationary, the angle of attack constantly changes as the blade moves around the circumference of the rotor disk. Other factors affecting angle of attack, over which the pilot has little control, are blade flapping, blade flexing, and gusty wind or turbulent air conditions. Angle of attack is one of the primary factors that determines amount of lift and drag produced by an airfoil.

Angle of Incidence

Angle of attack should not be confused with angle of incidence (blade pitch angle). Angle of incidence is the angle between the blade chord line and the plane of rotation of the rotor system. It is a mechanical angle rather than an aerodynamic angle:

In the absence of induced flow and/or aircraft airspeed, angle of attack and angle of incidence are the same. Whenever relative wind is modified by induced flow or aircraft airspeed, then angle of attack is different than angle of incidence.

3.3.4. Total aerodynamic force

A total aerodynamic force is generated when a stream of air flows over and under an airfoil that is moving through the air. The point at which the air separates to flow about the airfoil is called the point of impact:

A high pressure area or stagnation point is formed at the point of impact. Normally the high pressure area is located at the lower portion of the leading edge, depending on angle of attack. This high pressure area contributes to the overall force produced by the blade.

This picture also shows airflow lines that illustrate how the air moves about the airfoil section. Notice that the air is deflected downward as it passes under the airfoil and leaves the trailing edge. Remember Newton's third law which states "every action has an equal and opposite reaction." Since the air is being deflected downward, an equal and opposite force must be acting upward on the airfoil. This force adds to the total aerodynamic force developed by the airfoil. At very low or zero angles of attack, the deflection force or impact pressure may exert a zero positive force, or even a downward or negative force.

Air passing over the top of the airfoil produces aerodynamic force in another way. The shape of the airfoil causes a low pressure area above the airfoil according to Bernoulli's Principle, and the decrease in pressure on top of the airfoil exerts an upward aerodynamic force. Pressure differential between the upper and lower surface of the airfoil is quite small - in the vicinity of 1 percent. Even a small pressure differential produces substantial force when applied to the large area of a rotor blade.

The total aerodynamic force, sometimes called the resultant force, may be divided into two components called lift and drag. Lift acts on the airfoil in a direction perpendicular to the relative wind. Drag is the resistance or force that opposes the motion of the airfoil through the air. It acts on the airfoil in a direction parallel to the relative wind:

Many factors contribute to the total lift produced by an airfoil. Increased speed causes increased lift because a larger pressure differential is produced between the upper and lower surfaces. Lift does not increase in direct proportion to speed, but varies as the square of the speed. Thus, a blade travelling at 500 knots has four times the lift of the same blade travelling at only 250 knots. Lift also varies with the area of the blade. A blade area of 100 square feet will produce twice as much lift as a blade area of only 50 square feet. Angle of attack also has an effect on the lift produced. Lift increases as the angle of attack increases up to the stalling angle of attack. Stall angle varies with different blades and is the point at which airflow no longer follows the camber of the blade smoothly. Air density is another factor that directly influences lift.

Two design factors, airfoil shape and airfoil area are primary elements that determine how much lift and drag a blade will produce. Any change in these design factors will affect the forces produced.

Normally an increase in lift will also produce an increase in drag. Therefore, the airfoil is designed to produce the most lift and the least drag within normal speed ranges.

3.3.5. Drag in rotary aircraft

Drag is the force that opposes the motion of an aircraft through the air. Total drag produced by an aircraft is the sum of the profile drag, induced drag, and parasite drag. Total drag is primarily a function of airspeed. The airspeed that produces the lowest total drag normally determines the aircraft best-rate-of-climb speed, minimum rate-of-descent speed for autorotation, and maximum endurance speed.

The following picture illustrates the different forms of drag versus airspeed:

Profile drag is the drag incurred from frictional resistance of the blades passing through the air. It does not change significantly with angle of attack of the airfoil section, but increases moderately as airspeed increases.

Induced drag is the drag incurred as a result of production of lift. Higher angles of attack which produce more lift also produce increased induced drag. In rotary-wing aircraft, induced drag decreases with increased aircraft airspeed. The induced drag is the portion of the total aerodynamic force which is oriented in the direction opposing the movement of the airfoil. Think of it as lift which is in the wrong direction.

Parasite drag is the drag incurred from the nonlifting portions of the aircraft. It includes the form drag and skin friction associated with the fuselage, cockpit, engine cowlings, rotor hub, landing gear, and tail boom to mention a few. Parasite drag increases with airspeed.

Curve "A" shows that parasite drag is very low at slow airspeeds and increases with higher airspeeds. Parasite drag goes up at an increasing rate at airspeeds above the midrange.

Curve "B" shows how induced drag decreases as aircraft airspeed increases. At a hover, or at lower airspeeds, induced drag is highest. It decreases as airspeed increases and the helicopter moves into undisturbed air.

Curve "C" shows the profile drag curve. Profile drag remains relatively constant throughout the speed range with some increase at the higher airspeeds.

Curve "D" shows total drag and represents the sum of the other three curves. It identifies the airspeed range, line "E", at which total drag is lowest. That airspeed is the best airspeed for maximum endurance, best rate of climb, and minimum rate of descent in autorotation.

3.3.6. Centrifugal force

Helicopter rotor systems depend primarily on rotation to produce relative wind which develops the aerodynamic force required for flight. Because of its rotation and weight, the rotor system is subject to forces and moments peculiar to all rotating masses. One of the forces produced is centrifugal force. It is defined as the force that tends to make rotating bodies move away from the centre of rotation. Another force produced in the rotor system is centripetal force. It is the force that counteracts centrifugal force by keeping an object a certain radius from the axis of rotation.

The rotating blades of a helicopter produce very high centrifugal loads on the rotor head and blade attachment assemblies. As a matter of interest, centrifugal loads may be from 6 to 12 tons at the blade root of two to four passenger helicopters. Larger helicopters may develop up to 40 tons of centrifugal load on each blade root. In rotary-wing aircraft, centrifugal force is the dominant force affecting the rotor system. All other forces act to modify this force.

When the rotor blades are at rest, they droop due to their weight and span. In fully articulated systems, they rest against a static or droop stop which prevents the blade from descending so low it will strike the aircraft (or ground!). When the rotor system begins to turn, the blade starts to rise from the static position because of the centrifugal force. At operating speed, the blades extend straight out even though they are at flat pitch and are not producing lift.

As the helicopter develops lift during takeoff and flight, the blades rise above the "straight out" position and assume a coned position. Amount of coning depends on RPM, gross weight, and G-Forces experienced during flight. If RPM is held constant, coning increases as gross weight and G-force increase. If gross weight and G-forces are constant, decreasing RPM will cause increased coning. Excessive coning can occur if RPM gets too low, gross weight is too high, or if excessive G-forces are experienced. Excessive coning can cause undesirable stresses on the blade and a decrease of total lift because of a decrease in effective disk area:

Notice that the effective diameter of the rotor disk with increased coning is less than the diameter of the other disk with less coning. A smaller disk diameter has less potential to produce lift.

Centrifugal force and lift effects on the blade can be illustrated best by a vector. First look at a rotor shaft and blade just rotating:

Now look at the same rotor shaft and blade when a vertical force is pushing up on the tip of the blade:

The vertical force is lift produced when the blades assume a positive angle of attack. The horizontal force is caused by the centrifugal force due to rotation. Since one end of the blade is attached to the rotor shaft, it is not free to move. The other end can move and will assume a position that is the resultant of the forces acting on it:

The blade position is coned and is a resultant of the two forces, lift and centrifugal force, acting on it.

3.3.7. Rotational velocities

During hovering, airflow over the rotor blades is produced by rotation of the rotor system. Here is a picture showing a typical helicopter rotor system:

Blade speed near the main rotor shaft is much less because the distance traveled at the smaller radius is relatively small. At point "A", half way from the rotor shaft to the blade tip, the blade speed is only TBS knots which is one-half the tip speed. Speed at any point on the blades varies with the radius or distance from the center of the main rotor shaft. An extreme airspeed differential between the blade tip and root is the result. The lift differential between the blade root and tip is even larger because lift varies as the square of the speed. Therefore, when speed is doubled, lift is increased four times. This means that the lift at point "A" would be only one-fourth as much as lift at the blade tip (assuming the airfoil shape and angle of attack are the same at both points).

Because of the potential lift differential along the blade resulting primarily from speed variation, blades are designed with a twist. Blade twist provides a higher pitch angle at the root where speed is low and lower pitch angles nearer the tip where speed is higher. This design helps distribute the lift more evenly along the blade. It increases both the induced air velocity and the blade loading near the inboard section of the blade.

This picture compares the lift of a twisted and untwisted blade:

Note that the twisted blade generates more lift near the root and less lift at the tip than the untwisted blade.

3.3.8. Hovering

Hovering is the term applied when a helicopter maintains a constant position at a selected point, usually a few feet above the ground (but not always, helicopters can hover high in the air, given sufficient power). For a helicopter to hover, the main rotor must supply lift equal to the total weight of the helicopter. With the blades rotating at high velocity, an increase of blade pitch (angle of attack) would induce the necessary lift for a hover. The forces of lift and weight reach a state of balance during a stationary hover.

Hovering is actually an element of vertical flight. Assuming a no-wind condition, the tip-path plane of the blades will remain horizontal. If the angle of attack of the blades is increased while their velocity remains constant, additional vertical thrust is obtained. Thus, by upsetting the vertical balance of forces, helicopters can climb or descend vertically.

Airflow during hovering

At a hover, the rotor tip vortex (air swirl at the tip of the rotor blades) reduces the effectiveness of the outer blade portions. Also, the vortexes of the preceding blade severely affect the lift of the following blades. If the vortex made by one passing blade remains a vicious swirl for some number of seconds, then two blades operating at 350 RPM create 700 longlasting vortex patterns per minute. This continuous creation of new vortexes and ingestion of existing vortexes is a primary cause of high power requirements for hovering.

During hover, the rotor blades move large volumes of air in a downward direction. This pumping process uses lots of horsepower and accelerates the air to relatively high velocities. Air velocity under the helicopter may reach 60 to 100 knots, depending on the size of the rotor and the gross weight of the helicopter. The air flow pattern of a hovering helicopter is illustrated here:

Note how the downwash (induced flow) of air has introduced another element into the relative wind which alters the angle of attack of the airfoil. When there is no induced flow, the relative wind is opposite and parallel to the flight path of the airfoil. In the hovering case, the downward airflow alters the relative wind and changes the angle of attack so less aerodynamic force is produced. This condition requires the pilot to increase collective pitch to produce enough aerodynamic force to sustain a hover. Although this does increase the lift, it also increases the induced drag, and so total power required is higher.

3.3.9. Ground effect

The high power requirement needed to hover out of ground effect is reduced when operating in ground effect. Ground effect is a condition of improved performance encountered when operating near (within 1/2 rotor diameter) of the ground. It is due to the interference of the surface with the airflow pattern of the rotor system, and it is more pronounced the nearer the ground is approached. Increased blade efficiency while operating in ground effect is due to two separate and distinct phenomena.

First and most important is the reduction of the velocity of the induced airflow. Since the ground interrupts the airflow under the helicopter, the entire flow is altered. This reduces downward velocity of the induced flow. The result is less induced drag and a more vertical lift vector. The lift needed to sustain a hover can be produced with a reduced angle of attack and less power because of the more vertical lift vector:

The second phenomena is a reduction of the rotor tip vortex:

When operating in ground effect, the downward and outward airflow pattern tends to restrict vortex generation. This makes the outboard portion of the rotor blade more efficient and reduces overall system turbulence caused by ingestion and recirculation of the vortex swirls.

Rotor efficiency is increased by ground effect up to a height of about one rotor diameter for most helicopters. This figure illustrates the percent increase in rotor thrust experienced at various rotor heights:

At a rotor height of one-half rotor diameter, the thrust is increased about 7 percent. At rotor heights above one rotor diameter, the thrust increase is small and decreases to zero at a height of about 1 1/4 rotor diameters.

Maximum ground effect is accomplished when hovering over smooth paved surfaces. While hovering over tall grass, rough terrain, revetments, or water, ground effect may be seriously reduced. This phenomena is due to the partial breakdown and cancellation of ground effect and the return of large vortex patterns with increased downwash angles.

Two identical airfoils with equal blade pitch angles are compared in the following figure:

The top airfoil is out-of-ground-effect while the bottom airfoil is in-ground-effect. The airfoil that is in-ground-effect is more efficient because it operates at a larger angle of attack and produces a more vertical lift vector. Its increased efficiency results from a smaller downward induced wind velocity which increases angle of attack. The airfoil operating out-of-ground-effect is less efficient because of increased induced wind velocity which reduces angle of attack.

If a helicopter hovering out-of-ground-effect descends into a ground-effect hover, blade efficiency increases because of the more favourable induced flow. As efficiency of the rotor system increases, the pilot reduces blade pitch angle to remain in the ground-effect hover. Less power is required to maintain however in-ground-effect than for the out-of-ground-effect hover.