# Voltage stabilizer

A voltage stabilizer is an electronic device able to deliver relatively constant output voltage while input voltage and load current changes over time.

The voltage stabilizer is the shunt regulator such as a Zener diode or avalanche diode. Each of these devices begins conducting at a specified voltage and will conduct as much current as required to hold its terminal voltage to that specified voltage. Hence the shunt regulator can be viewed as the limited power parallel stabilizer. The shunt regulator output is used as a voltage reference.

The Zener diode and avalanche diode have opposite threshold voltage dependence on temperature. By connecting these two devices sequentially, it is possible to construct a voltage reference with improved thermal stability. Sometimes (mostly for the voltages around 5.6 V) both effects are combined in the same diode.

## Simple voltage stabilizer

In the simplest case emitter folower is used, the base of the regulating transistor is directly connected to the voltage reference:

The stabilizer uses the power source, having voltage Uin that may vary over time. It delivers the relatively constant voltage Uout. The output load RL can also vary over time. For such a device to work properly, the input voltage must be larger than the output voltage and Voltage drop must not exceed the limits of the transistor used.

The output voltage of the stabilizer is equal Vref + VBE where VBE is about 0.7v and depends on load current. If the output voltage drops below that limit, this increases the voltage difference between the base and emitter (Ube), opening the transistor and delivering more current. Delivering more current through the same output resistor RL increases the voltage again.

## Voltage stabilizer with an operational amplifier

The stability of the output voltage can be significantly increased by using the operational amplifier:

In this case, the operational amplifier opens the transistor more if the voltage at its inverting input drops significantly below the output of the voltage reference at the non-inverting input. Using the voltage divider (R1, R2 and R3) allows choice of the arbitrary output voltage between Uzand Uin.